## Slide 1
정밀한 온도 및
선명한 화질표시
다양한 비디오 포멧 지원을
통한 폭넓은 Application
초소형, 초경량, 저전력
및 편리한 설치
Quantum Eye MPDC
다목적 프로젝트용
실시간으로 정확한 인체발열측정이 가능한 고정밀 열화상+실화상 카메라입니다.
한화시스템의 특허받은 TRSM 모듈을 내장하여 다양한 환경에서
정확한 발열감지가 가능하고, 지능형 SW를 이용하여 실시간 발열자 및
마스크 미착용자를 찾아내어 출입통제가 가능합니다.
제슨나노보드를 이용하여 AI 기능 탑재가 가능하며,
다양한 프로젝트에 활용할 수 있습니다.
Key Features
듀얼 엣지 카메라
±0.3℃ 이내 온도 정확도(TRSM 장착시)
AI 기능 탑재 가능
Ethernet, HDMI, Audio In/Out, USB 등 다양한 인터페이스 제공
인체발열감지, 스마트팜, 가축질병 예방 등 다양한 분야 활용
Accuracy
Expandability
Efficiency

## Slide 2
Quantum Eye MPDC Technical Specifications
Color Cameral
Thermal Camera
Total pixels | 320(H) x 240(V) Pixels
Image Sensor Type | Micro Bolometer
Pixel Pitch | 12μm
Spectral Band | LWIR 8~14 µm
NETD | < 50mK @F/1.0
Field of View ( H x V ) | H: 28°, V: 21°, custom
Temperature Measurement Range | Febrile Sensing Mode : +30 °C ~ +40 °C Normal Mode : ~ +140 °C or ~ +500 °C
Temperature Accuracy | Febrile Sensing Mode : ±0.5 °C (w/ TRSM ±0.3 °C) Normal Mode : ±2°C or 2%
Frame Frequency | MAX 30 FPS
Image Sensor | 1/2.8" 2MP CMOS
Effective Pixels | 1920 x 1080
Max. Resolution | 2MP
Focal Length | 4 mm
Aperture | F1.6
Field of View | H: 87.6°, V: 46.4°, D: 104.5°
Frame Frequency | MAX 30 FPS
Focus Mode | Fixed
Interfacel
Other
Ethernet(Network) | 1000Base-T, RJ-45
Audio Input | 1 (Mic In)
Audio Output | 1 (Speaker Out)
Alarm Input | 1
Alarm Output | 1
Micro USB Connector | 2
Power LED | 1
Reset Botton | 1
HDMI | 1
Supply Voltage | DC +12V ±10%
Power | 20.0 Watt
Color | Black
Material | Aluminium
External Dimension (H x V x D) | 103.0mm x 118.0mm x 288.0mm (TRSM mounting)
Body Weight | 1.2 Kg
Operation Temperature | -10°C to +35°C (Humidity: 0%RH ~ 95%RH)
Storage Temperature | -30°C to +60°C (Humidity: 0%RH ~ 95%RH)

## Slide 3
Quantum Eye MPDC Dimensions
Exterior Dimension
Jetson nano Interface Dimension
Cover Dimension